## Slide 1: Fast Fourier Transform (FFT): for engineers in the making
Dr. Xiao Guo
School of EECS,
The University of Queensland,
Brisbane, Australia.
E-mail: xiao.guo@uq.edu.au
2026 July 14 at UQ

## Slide 2: Outline
Why Fourier Transformation (FT)?
Discrete FT(DFT) and Fast FT (FFT)
What happens and what is it?
How to do it fast?
When/Where we need it?
Test yourself 
Take home messages
Notes: Basically, no complicated math as our undergraduate stude in nts shut down the brain or close the video recording if full of math

## Slide 3: Why FT? “Unblend” a Baby Yoda Cocktail
FT helps to recognise the constituent components
Fresh Lime Juice
Grey goose vodka
Demerara sugar syrup
Peeled Kiwi
Ice
Let’s see a real example

## Slide 4: What is FT, DFT, FFT
FFT helps to recognise the constituent components
Fourier Transform
Digitise signals for digital devices
A bit slow
Much Faster DFT
Mathematically correct
Engineer Choice
Slow down – 1 min
IEEE Top 10 Algorithms of the 20th Century
ELEC2004
Notes: FT – time to frequency domain – small # of improtant freq. compoentns – same in cocktail small number of ingreadients
DFT – digital
FFT – quick
Skip how Gauss boringly did it, ridiculously boring math for physics students, not to mention engineering students

## Slide 5: Why do we need Fast Fourier Transformation (FFT)? (1)
A sensor gives us a complicated waveform, we need to understand it
Too complicated, what to do?
Normal
Stressful
Heart Attack
e.g., 70 beats/min
Heart signal generation: McSharry et al. IEEE Transactions on Biomedical Engineering 50.3 (2003): 289-294
Notes: Use the logic chain to show it can be used for all applications at the take-home message slide to call back
bpm = 70

## Slide 6: Why do we need Fast Fourier Transformation (FFT)? (2)
A sensor gives us a complicated waveform,
FFT helps to understand our data & make decisions 
Sensor (Hardware)
Let’s see it in Jupyter Notebook (30 sec).
Heart Attack
(Signals)
Data Collection
Frequency Info.
Decision (Action Required)
Muscle & noise: Friesen et al. IEEE Transactions on Biomedical Engineering 37.1 (1990): 85-98.
Notes: Why doctor looks at time-domain not frequency signal
-
The doctor is trained to read time-domain
If there is machine-assisted diagnosis, it is easier to check
Computer-assisted diagnosis

## Slide 7: Really, what happens?
We measured a complicated time-varying signal (in time domain).
FFT helps to find another way to present it (in frequency domain).
Major contributors plotted
Notes: Use the logic chain to show it can be used for all applications at the take-home message slide to call back

## Slide 8: What is Fast Fourier Transformation (FFT)? (1)
Fourier Integral  Discrete Fourier Transform (DFT)  FFT
Notes: Use the logic chain to show it can be used for all applications at the take-home message slide to call back

## Slide 9: What is Fast Fourier Transformation (FFT)? (2)
A fast version to implement Discrete Fourier Transform (DFT)
time-domain signal
If you want to code:
# N-slice of
# Spin frequency
Use Optimised FFT libraries, e.g., Numpy, pyFFTW (Python) or FFTW (C/C++) or Matlab
how an algorithm's execution time scales as the input size (n) grows
Y = fft(X)
Notes: Big O notation O(n) how an algorithm's execution time or memory usage scales as the input size (n) grows
Passing a float like 2000.0 will cause the function to fail.

## Slide 10: Why FFT is called fast FT?
FFT drops the number of multiplications:
drops to
In most of your cases, you will call libraries, no need to implement from scratch (except for fun)
Notes: Use the logic chain to show it can be used for all applications at the take-home message slide to call back

## Slide 11: FFT can be slow  zero padding signal length to
Pad your time-domain signal with zeros
Make a signal's length a power of two?
Modern FFT implementation handles non-power-of-two and prime lengths automatically.
We will see why in p.22
Notes: Use the logic chain to show it can be used for all applications at the take-home message slide to call back

## Slide 12: Zero padding can interpolate the frequency spectrum
Zero padding creates more frequency bins (visually smooths the plot)
Easier to identify the highest peak of an isolated signal
Note: not increase actual frequency resolution
Notes: Use the logic chain to show it can be used for all applications at the take-home message slide to call back

## Slide 13: FFT can give wrong information – sampling matters
Nyquist sampling theorem:
Use 2B Hz to sample B Hz
Antialising

## Slide 14: Application: Audio and Speech processing
Active noise cancelling
Have an animated step by step – struggled face to smile face in working environment
FFT converts the signal into individual frequency components, so we can find a way to cancel it
Play the audio signal – how it works
(high-pith noise)
Notes: Use the logic chain to show it can be used for all applications at the take-home message slide to call back

## Slide 15: Application: Audio and Speech processing
Active noise cancelling
Have an animated step by step – struggled face to smile face in working environment
FFT converts the signal into individual frequency components, so we can find a way to cancel it
1D Temporal-changing Signals
temporal frequency
time domain
Cycle per sec
Notes: Use the logic chain to show it can be used for all applications at the take-home message slide to call back
[\omega] = radians/sec
f = /sec or \omega = 2\pi f, f = \omega / 2\pi

## Slide 16: Application: Image Processing
Fine features like edges, beard, etc
Remove background noise
Low-pass filter
Filtered Image (x, y)
FFT of Image
Noisy Image (x, y)
Filtered Image (x, y)
High-pass filter
2D Static Images
spatial domain
spatial frequency
Cycle per metre or pixel
np.fft.ifft(X_ freq)
np.fft.ifft2(image_freq)
Notes: Use the logic chain to show it can be used for all applications at the take-home message slide to call back
[k] = radian/metre or radian/pixel

## Slide 17: fftshift: visualise FFT data in human’s intuition (1)
X = ifft2(Y)
X = ifft(Y)
Matlab
Y = fftshift(X)
Y = fft2(X)
Y = fft(X)
# Compute the FFT
fft_output = np.fft.fft(signal)
# Compute the raw frequency bins matching the FFT layout
freqs_raw = np.fft.fftfreq(len(signal), d=1/sampling_rate)
# Shift the frequencies and the FFT output to the center
fft_shifted = np.fft.fftshift(fft_output)
freqs_shifted = np.fft.fftshift(freqs_raw)
# Get the magnitude (amplitude) of the spectrum
amplitude = np.abs(fft_shifted) / len(signal)

## Slide 18: fftshift 1-D example (Matlab)
Matlab code
15 Hz example
Let’s see 2-D example, the next page
# frequency bin index, k
Python (Numpy), one line to get frequency axis (p.9)
An easier chioce:

## Slide 19: fftshift: visualise FFT data in human’s intuition (2)
2D FFT case
DC component will be at the upper-left corner
# 1. Forward Transform & Shift
X_image_2d_freq = np.fft.fft2(image)
X_image_2d_freq_shifted = np.fft.fftshift(X_image_2d_freq)
# 2. Correct Inverse Transform (Add the ifftshift step)
X_image_2d_freq_unshifted = np.fft.ifftshift(X_image_2d_freq_shifted)
X_reconstructed_2d_complex = np.fft.ifft2(X_image_2d_freq_unshifted)
# 3. take the amplitude
X_reconstructed_2d_abs = np.abs(X_reconstructed_2d_complex)

## Slide 20: fftshift: visualise FFT data in human’s intuition (2)
fftshift and then ifftshift back to the order that machine’s FFT prefers
# 1. Forward Transform & Shift
X_image_2d_freq = np.fft.fft2(image)
X_image_2d_freq_shifted = np.fft.fftshift(X_image_2d_freq)
# 2. Correct Inverse Transform (Add the ifftshift step)
X_image_2d_freq_unshifted = np.fft.ifftshift(X_image_2d_freq_shifted)
X_reconstructed_2d_complex = np.fft.ifft2(X_image_2d_freq_unshifted)
# 3. take the amplitude
X_reconstructed_2d_abs = np.abs(X_reconstructed_2d_complex)

## Slide 21: Take-home Messages (no complicated math)
Time-domain waveform and frequency-domain spectrum
Why it is named as “fast”?
When FFT is slow? Zero padding?
Sampling rate matters – avoid antialising – Nyquist theorem
Next, how does FFT work really?
FFTshift: shift DC component to the centre
If you don’t care FFT algorithm itself, you can relax now.
Notes: Mark the size darker

## Slide 22: How does FFT work really? Cooley-Tukey FFT
James William Cooley (1926 - 2016)
John Wilder Tukey
(1915 - 2000)
Math. Comp. 19 (1965), 297-301
"Divide and Conquer"
6 pages left
Notes: James W. Cooley – American Mathematician – PhD in Math from Columbia University (1961)
John Wilder Tukey – American Mathematician – PhD in Math from Princeton University (1939)

## Slide 23: How does FFT work really? Cooley-Tukey FFT
Divide a unit circle into N slices
A 1-million-point signal -> DFT: 1 trillion complex multiplications -> FFT: 20 million operations
"Divide and Conquer"
Radix-2 gets the attention
Example:
8-point FFT
Core idea:
multiple a rotating vector ,
the signal’s amplitude unchanged.
Even
Odd
Notes: Directly compute X(j) requires N^2 operations, operaion means “a complex multiplication followed by a complex addition”; A(k) are complex numbers
Cooley-Tukey FFT algorithm  less than 2N log_2 N operations, without requiring more data sotryage than is required for the given array A
s

## Slide 24: FFT’s beauty: “Divide and Conquer”
Even
Odd
1 signals of
8 points
2 signals of
4 points
4 signals of
2 points
[0]
[1]
[2]
[3]
[4]
[5]
[6]
[7]
Local index (even, odd)

## Slide 25: Butterfly Operation: 2-point FFT
"Divide and Conquer"
Radix-2 gets the attention
Example: 2-point FFT (N=2)
Time-domain
Frequency-domain
0
8
8
-8
Notes: Directly compute X(j) requires N^2 operations, operaion means “a complex multiplication followed by a complex addition”; A(k) are complex numbers
Cooley-Tukey FFT algorithm  less than 2N log_2 N operations, without requiring more data sotryage than is required for the given array A
2-point DFT = 2-point FFT
  DFT: k = 0,1,2,… N-1
  FFT: k = 0,1,…, N/2 - 1

## Slide 26: Example Question: how to get 2 point FFT?
10-sec
How to get 2-point FFT of this?

## Slide 27: Butterfly Operation: 4-point FFT
Example: 4-point FFT (N=4)
Time-domain
Frequency-domain
Even
Odd
2-point FFT
2-point FFT
If time allows, Jupyter Notebook demo
"Divide and Conquer"
Radix-2 gets the attention
Notes: Directly compute X(j) requires N^2 operations, operaion means “a complex multiplication followed by a complex addition”; A(k) are complex numbers
Cooley-Tukey FFT algorithm  less than 2N log_2 N operations, without requiring more data sotryage than is required for the given array A
s

## Slide 28: Butterfly Operation: N-point FFT
Input
FFT Output
10-sec

## Slide 29: How does FFT work really? Written in a matrix form
Prof. Gilbert Strang
(1934 - present)
https://ocw.mit.edu/courses/18-06-linear-algebra-spring-2010/resources/lecture-26-complex-matrices-fast-fourier-transform/
More math in below link (if interested)
Or even N-dimensional case
64-dimensional case
30-sec
Will not be in Exam 

## Slide 30: Take-home Messages
Time-domain waveform to frequency-domain spectrum
Why it is named as “fast”?
Sensor (hardware)
Sensor data
FFT
Frequency Information
Engineering Decision
When FFT is slow? Zero padding?
A journey from DFT to FFT
Sampling rate matters – avoid antialising – Nyquist theorem
Images: spatial domain to spatial frequency (2D)

## Slide 31: Q & A
xiaoguo1995.github.io
Thank you very much!
E-mail:
xiao.guo@uq.edu.au
Matrix form of FFT, 4 more slides
Notes: - Thank everyone for coming in and listening!

## Slide 32: How does FFT work really? Written in a matrix form
N-dimensional case for FFT
Will not be in Exam 
Permutation Matrix,
2N = 4 example
Odd pairs at the top of butterfly operations
Even pairs at the bottom (e.g., p.28)
Divide into 2 smaller DFTs, half of the sizes (p.24, you have done it!)
Butterfly Operations (p.28, you have seen this!)
Identity Matrix
Diagonal Matrix
The Twiddle Factor

## Slide 33: How does FFT work really? Written in a matrix form
N-dimensional case for FFT
2N = 4 example
recall (p.25):
Butterfly operations
Divide
Permutation
Butterfly operations
2N = 4

## Slide 34: How does FFT work really? Written in a matrix form
4-point FFT
2N = 4
We have
To obtain
Now, we get everything

## Slide 35: How does FFT work really? Written in a matrix form
Recall this! (p.24)
2N = 4 example
1st step: Permutation
Even
Odd
Even
Odd
input
shuffle
2nd step: Smaller 2–point FFT
3rd step: Butterfly Operations
Final result of FFT{0, 4, 8 ,12}
p.24: the same result!

## Slide 36: How does FFT work really? Written in a matrix form
Recall this! (p.24)
2N = 4 example
Even
Odd
p.24: the same result!
Final result of FFT{0, 4 ,8 ,12}

## Slide 37: Q & A
xiaoguo1995.github.io
Thank you very much!
E-mail:
xiao.guo@uq.edu.au
Notes: - Thank everyone for coming in and listening!